## Slide 1: Obstacle Avoiding and Auto-Parking Car

## Slide 2: Team Members
Amany Fathy
Hagar Tarek
Loreen Mohamed
Sama Ahmed
Nada Mohamed

## Slide 3: Table of contents 01 04 02 05 03 06
Problem Description
System Design
Solution Implementation
Flowchart
Cost Analysis
Conclusion

## Slide 4: Problem Description 01

## Slide 5: Problem Description
The car industry is one of the leading industries that has changed due to automation, with automation levels ranging from level 0 (no automation) to level 5 (fully autonomous cars).
Our objective was to design and implement an autonomous robot capable of avoiding obstacles and auto-park itself, making it a level 2 automation, partially automated.
The problem was implementing such an idea using non-industrial components, like an Arduino Uno board and a simple H-bridge motor driver.

## Slide 6: Challenges Faced in Tasks
Auto-parking
The number of sensors needed for optimal parking.
The challenges of parallel parking differ from those of perpendicular parking.
Choosing the best sensor to detect the presence of obstacles without adding unnecessary cost.
Choosing the best path to continue driving on when an obstacle is found.
Obstacle Avoidance

## Slide 7: System Design 02

## Slide 8: System Design
Arduino Uno
H-bridge
Motors
Ultrasonic Sensor
Button
Microcontroller
Integrated Circuit
Allow car to move
Measure distance to obstacles
Mode switching
Led
Indicate activating the parking mode

## Slide 9: System Design
Resistor
Wheel
Lithium Battery
Jumper Wires
Car Body
Lower voltage
Move car from point to another
Power Supply for the system
For electrical connections
Physical Structure
Breadboard
Reconfigurable Platform

## Slide 10: Solution Implementation 03

## Slide 11: Obstacle Avoidance
Sensor Integration and Obstacle Detection
Autonomous Navigation and Path Planning
The front ultrasonic sensor is attached to a servo, so it can turn around 180 degrees to check for any obstacles and find a clear path to drive on.
We used the NewPing library in Arduino to interface with ultrasonic distance sensors.
The obstacle avoidance logic is integrated into the car's movement, allowing it to adjust its path dynamically based on the detected obstacles.
`obstacle_avoid()` function is responsible for handling the obstacle avoidance logic.
It starts by reading the distance from the ultrasonic sensor using the `readPing()` function.
Obstacle Avoidance

## Slide 12: 2. Auto Parallel Parking
Sensor Integration
Parking Spot Detection
Solution relies on ultrasonic sensor readings.
Three ultrasonics : Front, Back, and Side.
We used the Ultrasonic library on Arduino to work with ultrasonic distance sensors.
`Check_Parking_Spot()` is responsible for detecting the parking spot and confirming its dimensions.
Front and side ultrasonic sensors are used to gather distance information.
`Find_Park()` coordinates the parallel parking strategy.
The parking status is 3, meaning that the parking spot is available, so the car is stopped, and the parking status is set to 4 (start parallel parking).
Parallel Parking Strategy

## Slide 13: Flowchart 04

## Slide 14: Obstacle Avoidance

## Slide 15: Parallel Auto-parking

## Slide 16: Cost Analysis 05

## Slide 17: Cost Analysis
Component | Units | Unit Price | Total Price
Car Body | 1 | 200 | 200
Arduino UNO | 1 | 465 | 465
Bread Board | 1 | 15 | 15
Jumpers | 32 | 1 | 32
Ultrasonic Sensor | 3 | 45 | 135
US Holder | 2 | 15 | 30
Lithium Battery | 2 | 65 | 130
Component | Units | Unit Price | Total Price
Battery Holder | 1 | 21 | 21
H Bridge | 1 | 90 | 90
Servo | 1 | 110 | 110
Resistor | 1 | 0.5 | 0.5
Button | 1 | 2.5 | 2.5
Free Wheel | 1 | 35 | 35
Led | 1 | 1 | 1

## Slide 18: Cost Analysis
The total cost of 1,267 EGP for the autonomous car system is an appropriate and justified cost for the following reasons:
The selection of each component was carefully considered to balance functionality, performance, and cost-effectiveness.
By choosing cost-effective yet reliable components, such as the Arduino Uno, ultrasonic sensors, and basic electronic parts, the project was able to keep the overall cost at a reasonable level.

## Slide 19: Ultrasonic Sensor or Camera ?
Cost
The camera’s cost is estimated to be 800 EGP, while the three ultrasonic sensors together cost 135 EGP, so we were able to save about 665 EGP.
Ultrasonic Sensors are generally more affordable.
Camera-based systems often require more complex image processing and algorithms, which can increase the overall complexity and cost of the project.
Ultrasonic sensors provide direct distance measurements
Simplicity
In this project, the decision was made to use three ultrasonic sensors instead of a camera-based system. WHY ?

## Slide 20: Task Videos

## Slide 21: Obstacle Avoidance

## Slide 22: Parallel Auto-Parking

## Slide 23: Conclusion 06

## Slide 24: Coclusion
In conclusion, our autonomous car project, which focused on object avoidance and parallel parking, successfully met its goals and objectives through the effective use of embedded systems. By integrating ultrasonic sensors, we enabled the car to accurately perceive its surroundings, ensuring reliable detection of obstacles and precise execution of parallel parking strategies. The seamless interaction between hardware components and software algorithms demonstrated the viability of ultrasonic sensor technology in enhancing the capabilities of autonomous vehicles.

## Slide 25: Thanks !